## Slide 1: NATIONAL INSTITUTE OF TECHNOLGY ANDHRA PRADESH
COURSE INSTRUCTOR : | DR. V. PRAKASH SINGH
STUDENT NAME : | P. SAI ADITYA REDDY
ROLL NUMBER : | 620226
DEPARTMENT OF ELECTRONICS AND COMMUNICATIONS ENGINEERING
EC304- MICROCONTROLLERS
ASSIGNMENT - 1

## Slide 2: 8051 - DS1307 REAL TIME CLOCK INTERFACING USING I2C

## Slide 3: ROADMAP
1
3
5
6
4
2
First we will look into the protocol of I2C
Second we look into the DS1307
We are going to interface DS1307 RTC with 8051
Then we look into the implementation of I2C in Embedded C
And also DS1307Real Time Clock implementation in Embedded C
Simulate and Verify

## Slide 4: 1. I2C COMMUNICATION PROTOCOL
Let’s start with the protocol….

## Slide 5: I2C COMMUNICATION
I2C protocol was invented by Philips semiconductors in the 1980s, to provide easy onboard communications between a CPU and various peripheral chips. I²C stands for Inter-Integrated Circuit. It is a short distance serial interface that requires only two bus lines for bi-directional data transfer.

## Slide 6: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
An I2C bus contains a clock line (SCK) and data line (SDA).

## Slide 7
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
An I2C link is always half-duplex, meaning that all devices share the data line with only one device transmitting at any given time.

## Slide 8
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
An I2C bus ALWAYS needs external pull-up resistors on each of its lines.
These can’t be implemented on the MCU because the resistor function is only available when the port is configured as an INPUT.
Since I2C is bidirectional, we never know wither the pin will be an input or output.

## Slide 9: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Master – the device that initiates communication and controls the clock.
Multiple masters are also supported on an I2C bus.

## Slide 10: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Slave – a device on the bus that is read or written to, but does not initiate transmission or provide a clock.
Slave address – a unique and predetermined address for each slave on the bus.
This address is used by the master to indicate which slave it wants to communicate with.

## Slide 11: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
A master initiates a new message by generating a START (S) condition by pulling SDA LOW while SCL is still HIGH.
As soon as the START condition is generated, the SCL will be pulled LOW and start pulsing to provide the clock for the message.

## Slide 12: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The master is responsible for pulsing the clock.

## Slide 13: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Each clock pulse within the I2C message is numbered by periods.
Both the master and the slaves count the number of periods that have occurred since the message started in order to know when certain frames and signals should be present.

## Slide 14: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
After the master generates the START condition, it first sends the slave address that it wishes to communicate with.
I2C slave addresses can either be 7-bit (default) or 10-bit.

## Slide 15: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The slave address is followed by the read/write signal indicating which type of transaction is being requested in the message.
The START condition, slave address, and read/write signal constitute periods 1 → 8.

## Slide 16: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Period 9 of the message is reserved for the slave acknowledge (ACK) or no-acknowledge (NACK) signal.
After the slave address and read/write signal are sent by the master, each slave on the bus checks whether it is being addressed.

## Slide 17: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
If a slave exists with the specified slave address, it will send an ACK signal back to the master by pulling SDA LOW.
If no device exists with the specified slave address, no device will pull down SDA. This will result in period 9 remaining HIGH and will be interpreted as a NACK.

## Slide 18: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
If the master sees the ACK signal, it knows a slave exists with the specified address and proceeds with the message.

## Slide 19: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
After each byte is sent, the receiving device sends an ACK signal indicating that it successfully received the data.

## Slide 20: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
A STOP condition occurs when there is a LOW-to-HIGH transition on SDA while SCL is HIGH.
Once, SDA goes HIGH, SCL also remains HIGH indicating that the bus is idle again.

## Slide 21: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
A NACK in period 9 tells the master that no slave exists with the specified address.
The master then generates a STOP condition and ends the message.
NACK

## Slide 22: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol

## Slide 23: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
When the master is writing to a slave, the master sends the 8-bits of data and the slave produces the ACK/NACK signal.
When the master is reading from a slave, the slave sends the 8-bits of data and the master produces the ACK/NACK signal.
After the data has been sent and acknowledged, the master can end the message by generating the STOP condition anytime.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada

## Slide 24: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The Master can send multiple data bytes in a single message.

## Slide 25: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Review of the Basic I2C Message Structure

## Slide 26: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
I2C devices contain individual registers that hold their information.
In the simplest case, an I2C device contains only a single register.

## Slide 27
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Writing to a slave with a single register.
  The master initiates the message by sending the S bit.
  The master provides the slave address and a WRITE signal.
  The slave ACKs to indicate it is ready.
  The master writes the data.
  The slave sends an ACK that it got the data.
  The master ends the message by sending the P bit.
No register address is needed.

## Slide 28: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
Reading from a slave with a single register.
  The master initiates the message by sending the S bit.
  The master provides the slave address and a WRITE signal.
  The slave ACKs to indicate it is ready.
  The slave sends the data.
  The master sends a NACK to stop the slave from sending more data.
  The master ends the message by sending the P bit.
No register address is needed.

## Slide 29: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
When an I2C device has multiple registers, each is assigned a register address.
To access a specific register in the slave, the master needs to provide the register address in the message.

## Slide 30: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
For a write transaction, the master generates an I2C message that first provides the slave address, then provides the register address to access, then provides the data to be written.
After each frame, the slave sends an ACK signal.

## Slide 31: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The master can also write a block of data to registers.
The slave automatically increments the starting address after each byte of data is written.
The master still sends the slave address, the write signal, and the starting register address.
The next byte of data that is sent goes into the first register address location.

## Slide 32: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The slave will continue to increment its register address until it sees the STOP condition generated by the master.
Check the slave’s datasheet for details!!!

## Slide 33: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
When reading from a device that contains multiple registers, two message are needed.

## Slide 34: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
When reading from a device that contains multiple registers, two message are needed.
The first message sets the register address within the slave that will be read from using a write transaction.
The first message puts the slave into a mode where it’s expecting a second message that will read data from the register address that was just sent.

## Slide 35: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The second message performs a read transaction that retrieves the data from the register address sent in the first message.

## Slide 36: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
1. The I2C Protocol
The master can also read blocks of data from a slave.
In this situation, the master still sends two messages, the first setting the register address and the second retrieving the data.
In the second message, the master continually sends SCL pulses to read as many bytes as it wants prior to generating the STOP condition.

## Slide 37
IMPLEMENTATION OF I2C IN KEIL
Let look at the implementation of I2C using Embedded C for 8051

## Slide 38: 2. DS1307 REAL TIME CLOCK

## Slide 39
CIRCUIT DIAGRAM OF DS1307 FOR INTERFACING
(refer DS1307 datasheet)

## Slide 40
TIMEKEEPER REGISTERS OF DS1307 RTC
(refer DS1307 datasheet)

## Slide 41
CONTROL REGISTER
(refer the DS1307 datasheet)
The DS1307 control register is used to control the operation of the SQW/OUT pin.
Bit 7: Output Control (OUT). This bit controls the output level of the SQW/OUT pin when the square-wave output
is disabled. If SQWE = 0, the logic level on the SQW/OUT pin is 1 if OUT = 1 and is 0 if OUT = 0. On initial
application of power to the device, this bit is typically set to a 0.
Bit 4: Square-Wave Enable (SQWE). This bit, when set to logic 1, enables the oscillator output. The frequency of
the square-wave output depends upon the value of the RS0 and RS1 bits. With the square-wave output set to 1Hz,
the clock registers update on the falling edge of the square wave. On initial application of power to the device, this
bit is typically set to a 0.
Bits 1 and 0: Rate Select (RS[1:0]). These bits control the frequency of the square-wave output when the square wave output has been enabled. The following table lists the square-wave frequencies that can be selected with the RS bits. On initial application of power to the device, these bits are typically set to a 1.

## Slide 42
PROGRAM TO INTERFACE DS1307 IN KEIL
Let look at the implementation of DS1307 using Embedded C for 8051

## Slide 43
PROTEUS SIMULATION OF RTC WITH 8051
Let look at the simulation of RTC with 8051 using I2C

## Slide 44
Conclusion…..
In this way we are able to communicate with the external peripherals using I2C
We can also communicate with multiple peripherals
In this project only DS1307 RTC is interfaced using I2C
We can also interface EEPROM using I2C
We are able to observe the desired results in proteus simulation

## Slide 45
References …
Embedded Systems Design using the MSP430FR2355 LaunchPad by BROCK J.LaMeres
DS1307 Datasheet from Maxim Integrated Products.

## Slide 46: THANKS!
Any questions?
You can find me at:
620226@student.nitandhra.ac.in